FUSE	Extended	168	328
1111	Not used	1111
1	Not used	1
1	Boot size SZ1 (smallest)	1	BOD2
1	Boot size SZ0	0	BOD1
1	Reset vector	1	BOD0

Fuse high
1	Ext Reset	1
1	Debug	1
0	Serial prog	0
1	Watch dog	1
0	EEPROM	0
1	BodLeveL2	1	SZ1
0	BodLeveL1	2.7V	1	SZ0
1	BodLeveL0	1	Reset Vector

Fuse	168 and 328
1	Clock Divide
1	Clock output
0	SUT1	BOD enabled 14CK
0	SUT0
0	CKSEL3	Default 8MHz RC internal
0	CKSEL2
1	CKSEL1
0	CKSEL0

Fuses	Extended	High	Low
For Atmega 168	0xFF	D5	C2
For Atmega 328	0xFD	D7	C2
Memory Lock	No memory protection needed set to 0xFF

Valuers used in “UNO as AVR programmer”
168
Fuse_Ex = 0xFF;	Same
Fuse_H = 0xD7;	Different BOD
Fuse_L = 0xE2;	Different
Lock = 0xFF;	Different SUT

328
Fuse_Ex = 0xFF;	Different BOD
Fuse_H = 0xD7;	Same
Fuse_L = 0xE2;	Different SUT
Lock = 0xFF;	No LOCK
Note 168 and 328 fuses originally chosen top be the same.

Migration of mini-OS and pcb_bootloader from Atmega 168 to 328 user device

bootloader_header file:	No changes	(Target only detects Atmega devices)
Bootloader_main_with_OS_reset.c
1.	PageSZ, Pamask, FlashSZ updated for Atmega 328 target
2.	Text	“Send file (Atmega328)”
3.	Fuse bytes updated

Bootloader_SW and HW subs no changes needed

pcb_bootloader_CA and CC	Introductory text only needed changing

Using the mini-OS with reset

Compile Bootloader for CA and CC displays using the resource file	Bootloader_main_with_OS_reset.c	DONE

In user Projects
Change definition of waiting_for_I2C_master
from
TWCR = (1 << TWEA) | (1 << TWEN);\
while (!(TWCR & (1 << TWINT)));\
TWDR;
to
TWCR = (1 << TWEA) | (1 << TWEN);\
{int m = 0; while((!(TWCR & (1 << TWINT))) && (m++ < 5000))wdr();\
if (m >= 4999){sei(); while((!(TWCR & (1 << TWINT))));}}\
TWDR;
DONE

Add ISR routine	To user projects
ISR (WDT_vect){
……	//Project dependent eeprom saves
…...
Reset_Atmega328;
Reset_I2C;
while(1);}

Add these definitions to the user project header file

#define Reset_Atmega328 \
PORTC |= (1 << PC3);\
DDRC |= (1 << PC3);\
_delay_ms(1);\
PORTC &= (~((1 << PC3)));\
_delay_ms(1);\
PORTC |= (1 << PC3);

#define Reset_I2C \
DDRB |= (1 << DDB4);\
PORTB &= (~(1 << PORTB4));