FUSE	Extended	168	328
1111	Not used	1111
1	Not used	1
1	Boot size SZ1 (smallest)	1	BOD2
1	Boot size SZ0	0	BOD1
1	Reset vector	1	BOD0

Fuse high
1	Ext Reset	1
1	Debug	1
0	Serial prog	0
1	Watch dog	1
0	EEPROM	0
1	BodLeveL2	1	SZ1
0	BodLeveL1	2.7V	1	SZ0
1	BodLeveL0	1	Reset Vector

Fuse	168 and 328
1	Clock Divide
1	Clock output
0	SUT1	BOD enabled 14CK
0	SUT0
0	CKSEL3	Default 8MHz RC internal
0	CKSEL2
1	CKSEL1
0	CKSEL0

Fuses	Extended	High	Low
For Atmega 168	0xFF	D5	C2
For Atmega 328	0xFD	D7	C2
Memory Lock	No memory protection needed set to 0xFF

Valuers used in “UNO as AVR programmer”
168
Fuse_Ex = 0xFF;	Same
Fuse_H = 0xD7;	Different BOD
Fuse_L = 0xE2;	Different
Lock = 0xFF;	Different SUT

328
Fuse_Ex = 0xFF;	Different BOD
Fuse_H = 0xD7;	Same
Fuse_L = 0xE2;	Different SUT
Lock = 0xFF;	No LOCK
Note 168 and 328 fuses originally chosen top be the same.

Migration of mini-OS and pcb_bootloader from Atmega 168 to 328 user device

bootloader_header file:	No changes	(Target only detects Atmega devices)
Bootloader_main_with_OS_reset.c
1.	PageSZ, Pamask, FlashSZ updated for Atmega 328 target
2.	Text	“Send file (Atmega328)”
3.	Fuse bytes updated

Bootloader_SW and HW subs no changes needed

pcb_bootloader_CA and CC	Introductory text only needed changing

Using the mini-OS with reset

Compile Bootloader for CA and CC displays using the resource file
 1	Bootloader_main_with_OS_reset.c	DONE

In user Projects
2	Change definition of waiting_for_I2C_master
from
TWCR = (1 << TWEA) | (1 << TWEN);\
while (!(TWCR & (1 << TWINT)));\
TWDR;
to
TWCR = (1 << TWEA) | (1 << TWEN);\
{int m = 0; while((!(TWCR & (1 << TWINT))) && (m++ < 5000))wdr();\
if (m >= 4999){sei(); while((!(TWCR & (1 << TWINT))));}}\
TWDR;
DONE

3	Add ISR routine	To user projects
ISR (WDT_vect){
……	//Project dependent eeprom saves
…...
Reset_Atmega328;
Reset_I2C;
while(1);}

Add these definitions to the user project header file

4	#define Reset_Atmega328 \
PORTC |= (1 << PC3);\
DDRC |= (1 << PC3);\
_delay_ms(1);\
PORTC &= (~((1 << PC3)));\
_delay_ms(1);\
PORTC |= (1 << PC3);	//Note 14CK delay present before jump to 0x7000
//Must check that this is enough or swap reset lines in ISR
5	#define Reset_I2C \
DDRB |= (1 << DDB4);\
PORTB &= (~(1 << PORTB4));

6	#define Thirty_two_ms_WDT_with_interrupt \
wdr();\
SREG_BKP = SREG;\
cli();\
WDTCSR |= (1 <<WDCE) | (1<< WDE);\
WDTCSR = (1<< WDE) | (1 << WDIE) | (1 << WDP0);\
MCUSR=0;\
SREG = SREG_BKP;

7	Add this line immediately after the setup_HW macro
Thirty_two_ms_WDT_with_interrupt;

8	Add this declaration to top of User Project header file
unsigned char SREG_BKP;

9	Ensure the line
wdr();
is added everywhere needed to prevent spurious watch dog reset

Do all header file changes but only add the line
Thirty_two_ms_WDT_with_interrupt;
wdr();
and the ISR routine
to the user project if wanting to implement mini-OS reset which is rarely needed

In bootloader:
Verification takes too long, either miss it out or divide flash size by 4 in verification routine.
NOT DONE YET